## Slide 1: ESL Server Spec.
WISE-EC
Oct, 2017

## Slide 2: ESL System Architecture 1/ 2
Application Server
Router
ESL
Gateway
ESL Server

## Slide 3: Outline
ESL SW Architecture
ESL Server Requirement List
  Device Management
  Service Management
  Account Management
  External Data Exchange Interface
  Image Generator
Competitor’s UI
  Competitor1
    Item/Device Management
    Report
  Competitor2
    Item/Device Management
    Image Generator

## Slide 4: Gateway SW Architecture
WISE-3640
Timer
UART
RTC
DDR
USB
IPQ4029
Flash
RF2.4G
System Tasks
MCU / RF Chip: TI CC2538
OpenWRT
Task synchronization
initialization and starting
Message exchange between tasks
Power management
Task registration
OSAL
Interrupt handling
Timer
Memory allocation
Mini PEIe
WIFI/Ethernet
Application layer
Gateway Device/Service/account Mgt SW & API
Nwk
Layer
Security AAA/VPN/Firewall
Handshaking
Mac
Port
Mgt
Jumbo frame
WAN/LAN Config
MQTT broker
WISE-agent
Encryption
DHCP
Connectivity: Zigbee
APS
Mac
Network Layer
Application Layer
Data Service
Frame Security
Mgt Service
Routing
AF: Tag ApplicationObject:
-Send Data
-Received Data
Zigbee Device
Object
Distributed address
Route Maintenance
Route discovery
End point binding
Build group
OTA frame
Mgt PANs
ZDP: Device & service discovery
OS Abstraction Layer APIs
GUI
Device Mgt
Gateway config
SW Owner :
1.Gsmartek in OSAL & OpenWRT’s Tag Mgt SW in Red.
2.CharlesH in GUI.
Service Mgt

## Slide 5: Admin. Operation on Cloud/ESL Server
ESL Server
WISE-3640
Gateway
RESTful
API
Tag Mapping Data
-update TAG data & schedule
GUI
Device Mgt
1. Device monitor
-Tag battery alert
-Tag status report
2.Remote control
-import tag-list for legal join
Image Generator
1.Generate image file (full and partial) and preview
2.Image file transform to ESL system’s format and zip
3. Provide Api for tag image update
Service Mgt
-FTP:OTA FW /image to device
-Execute action
e.g. tag image update : schedule / image generate
WISE-3240
Router
Device Mgt
Build group : connect to gateway
End point binding
Service Mgt
FTP: OTA FW/image to tag
FTP: OTA FW on Router
API
Device Mgt
1. Device monitor
-Tag battery alert
-Tag status report
2.Remote control
-Provide tag-list for router
-Tag/Router join
Service Mgt
-FTP: OTA FW/image to Tag/Router
-Execute action on Tag/Router
e.g. tag image update : schedule / image generate
Database
GUI
Gateway Config
Device Mgt :
-device monitor,Remote control
Service Mgt
-OTA FW & image
Admin
統操作端
Account Mgt
Account
Account Role
Permission for account and Role/group

## Slide 6: End user Operation on 醫護系統
Image
generator
RESTful
API
Tag Mapping Data
Update to ESL Server
-update data of the Tag
-update schedule of the Tag
ESL
Server
Device Mgt
1. Device monitor
-Tag battery alert
-Tag status report
2.Remote control
-import tag-list for legal join
Service Mgt
-FTP:OTA FW /image to device
-Execute action
e.g. tag image update : schedule / image
Account Mgt
Account
Account Role
Permission for account and Role/group
Database
POS/醫護系統操作端
Mapping list
2.Image generate
更新價錢
在區塊B
版型
B (X,Y,X長度,Y長度) ->價錢
產出圖檔
3.Image transformer
1. Image transformer
2.Compression
From Gsmartek.
data
1.Layout editor
第一次需排版ESL畫面,
定義區塊 ->資料
A (X,Y,X長度,Y長度) ->品名
B (X,Y,X長度,Y長度) ->價錢
C (X,Y,X長度,Y長度) ->貨號
D (X,Y,X長度,Y長度) ->庫存
版型
Schedule
排版
價錢
Notes: Image Generator
1. ESL 排版軟體 定義區塊
      A (X,Y,X長度,Y長度) ->品名
      B (X,Y,X長度,Y長度) ->價錢
      C (X,Y,X長度,Y長度) ->貨號
      D (X,Y,X長度,Y長度) ->庫存
2.Generate image file (full and partial) and preview
3.Image file transform to ESL system’s format and zip
get final DATA to ESL Server

## Slide 7: ESL Server Device Mgt
系統管理
  Gateway\Router\Tag狀態監控
    Tag 電量
    裝置類型
    裝置資訊(Mac address, IP address )
    Firmware Version
    RSSI
    連線狀態
    拓樸架構
    最後更新時間
    Preview Tag上的image
  Gateway\Router\Tag參數設定
    Tag Report 週期
    Tag Data Request 週期
    事件逾時參數
  Tag 註冊\移除
    Tag 綁定Item\解除綁定Item
    Tag 上顯示的資訊會與已存在的該位置的實物呼應，例如:Tag 顯示貨架上的某商品的價格、Tag 顯示病床上病人的資訊，在之後的敘述以”Item”代表此實物
提供易於手持裝置上使用的操作介面，例如APP 或 Mobile Web
  Item 的資料管理
  密鑰管理
  License 管理
Report
  活動紀錄
  更新成功率
  電池壽命分布比率

## Slide 8: ESL Server Service Mgt
Image update
  事件觸發更新image
  例如後臺價格更新或是人員手動更新…
  排程更新image
  例如於促銷時間將tag 更新至新價格
  管理Tag 對應的template
  失敗重傳機制
FOTA
  Firmware 匯入介面
  排程更新firmware

## Slide 9: ESL Server Account mgt
User management
  權限管控
  User 新增\刪除\修改

## Slide 10: ESL Server 外部資料交換介面
外部資料交換介面
  檔案交換介面
  資料庫交換介面
  依客戶需求客製化資料交換介面

## Slide 11: Image Generator
Image creator
  根據將欲顯示的數值帶入Template 產生圖片
Template editor
  提供圖形化介面讓客戶可以透過拖拉元件的方式，設計並產生所需的Template file

## Slide 12: Competitor UI

## Slide 13: Competitor1’s UI – Item (產品/病床 Info. ) 1/3

## Slide 14: Competitor1’s UI – Item (產品/病床 Info. )2/3

## Slide 15: Competitor1’s UI – Item (產品/病床 Info. )3/3

## Slide 16: Competitor1’s UI – Device Mgt 1/4

## Slide 17: Competitor1’s UI – Device Mgt 2/4

## Slide 18: Competitor1’s UI – Device Mgt 3/4

## Slide 19: Competitor1’s UI – Device Mgt 4/4

## Slide 20: Competitor2’s UI – Device Mgt 1/2

## Slide 21: Competitor2’s UI – Device Mgt 2/2

## Slide 22: Competitor2’s UI – Image Generator

## Slide 23
Thank You!