## Slide 1
EWM-W168 porting note
Rsb-4411
Liszt Kao, ESS-RISC, Embedded-IoT
2019/04/16

## Slide 2: Outline
Wi-Fi driver
Bluetooth

## Slide 3: Wi-Fi Driver
Add configuration in Makefile
  CONFIG_PLATFORM_ARM_IMX6QD = y
  CONFIG_RTL8822B = y
  ifeq ($(CONFIG_PLATFORM_ARM_IMX6QD), y)
  EXTRA_CFLAGS += -DCONFIG_LITTLE_ENDIAN -DCONFIG_PLATFORM_ANDROID
  EXTRA_CFLAGS += -DCONFIG_CONCURRENT_MODE
  EXTRA_CFLAGS += -DCONFIG_IOCTL_CFG80211 -DRTW_USE_CFG80211_STA_EVENT
  EXTRA_CFLAGS += -DCONFIG_RADIO_WORKARCH := arm
  CROSS_COMPILE :=../prebuilts/gcc/linux-x86/arm/arm-linux-androideabi-4.9/bin/arm-linux-androideabi-
  KSRC :=../kernel_imx
  MODULE_NAME := 8822be
  endif
Build Command
  make ARCH=arm KSRC=../kernel_imx/ CROSS_COMPILE=../prebuilts/gcc/linux-x86/arm/arm-linux-androideabi-4.9/bin/arm-linux-androideabi-

## Slide 4: Bluetooth
Hal
  The default Bluetooth have to be removed in ~/system/bt
  Remove ADD-ON configuration in rtkbt.mk
    #BOARD_HAVE_BLUETOOTH_RTK_ADDON := basic
Driver
  Add pid/vid on rtk_btusb.c and set up module config & fw.
  Using vfs_read instead of bdaddr_file->f_op->read because of read function is null.(header file)
  Driver read MAC address at this (advantech.sh echo an new one while system boot up first time)
    #define BDADDR_FILE "/data/misc/bluetooth/bdaddr“
  For both config & fw be loaded, the firmware path /system/etc/firmware/ have to be included.(PATCH not included)

## Slide 5: Bluetooth
Build driver module
  export PATH=$PATH
  export ARCH=arm
  export CROSS_COMPILE=${PWD}/prebuilts/gcc/linux-x86/arm/arm-linux-androideabi-4.9/bin/arm-linux-androideabi-
  OLD_PATH=${PATH}
  export PATH=${PWD}/bootable/bootloader/uboot-imx/tools/:${PATH}
  pushd ${PWD}/kernel_imx
  make imx_v7_adv_android_defconfig
  make modules -j$COREpopd
  export PATH=${OLD_PATH}

## Slide 6
Go Together,
We Go Far and Grow Big